## Slide 1: Impulse Space Onsite Presentation
3/10/2025
Rajan Phadnis

## Slide 2: Agenda
About Me
Internship Highlight: Northrop Grumman
Internship Highlight: SpaceX
About PSP and CMS
Upper Plumbing
  Sizing (Python and Excel)
  System Design
  Bang-Bang Manifold Design
  Manufacturing
  Bang-Bang Test Campaign
  Full Vehicle Ops

## Slide 3: About Me
Born in New York, grew up overseas, moved back to the US for high school
  Fluent in French
  Visited 60+ countries
Graduated from Purdue in December with a BS in Aeronautical & Astronautical engineering
Part of Purdue Space Program’s Liquids team
2 years of internships:
  7 months: T4
  4 months: Sentinel
  4 months: Antares
  5 months: Falcon
  4 months: Raptor
@ Northrop Grumman
@ SpaceX

## Slide 4: Internship Highlights: Northrop Grumman
Designed a mating ring for Cygnus to Antares, Falcon 9, MLV (Firefly)
Sized Sentinel’s TVC system
Propulsion system optimizations for a classified program
Designed vehicle conditioning GSE for a classified program

## Slide 5: Internship Highlights: SpaceX
Raptor
Owned nozzle heating for engine startup development
Designed tooling to reduce nozzle production downtime
Built/plumbed various systems around the factory
Falcon
Cut QD setup time by 10%+ via automation
Deleted 400+ engineering labour hours via autosequences
Automated away most (if not all) nominal checkout data reviews

## Slide 6: Purdue Space Program - Liquids
Engine
Lower
Plumbing
Methane Tank
LOx Tank
Upper Plumbing
Helium COPV
Nosecone/Recovery
Purdue’s student-run liquid rocketry team
Launch of CraterMaker Special…soon
  900lbf engine, targeting 40,000ft apogee
  Methalox vehicle + helium press system

## Slide 7: CMS & Me: Upper Plumbing & GSE
Upper Plumbing:
  Sizing, design and simulation
  Manufacturing, qualification and test
Avionics packaging and bang-bang integration
GSE buildup to support test and flight ops (fluids + daq)
Data visualization platform

## Slide 8: Upper Plumbing Goals
Press the tanks to flight pressures (LNG: 315psia, Lox: 326psia) and keep them within +/- 15psi
Fill the vehicle’s commodities tank and press to 4950psia
Handle nominal and most emergency vent scenarios

## Slide 9: Overview
Sizing
  Python & Excel
System Design
  Fluids System Design
  Bang-Bang Manifold
Manufacturing
Subsystem Test Campaign
Vehicle Test Campaign

## Slide 10: Sizing Sim: Python
Goal was to create a model that could:
  Size orifices, COPV, line sizes, and pressure spikes
  Form a baseline for test data comparison
  Execute on a faster-than-realtime basis
Iterative time-based approach, largely gated by coolprop latency
COPV end state determined isentropically
Expansion across bang-bang is isenthalpic (Joule-Thomson effect applies) – lookup enthalpies via knowns and coolprop
Had a lot of issues with Coolprop and units – paused work to get basic sizing done in Excel instead

## Slide 11: Sizing Sim: Back to Basics
Used these calculators to find:
Solenoid Cv
Max allowable cycle time
Pressure spike
Min relief/burst disk/QD Cv
Req’d COPV size and prepress
System mass flows
LNG: 38%54%
LOx: 64%  90%
Modeled start and end conditions as if they were the steady-state conditions
Sized solenoids to hit within 25%-75% duty cycle to avoid high pressure spikes and loss of press authority
COPV end pressure was 2x prop tank MEOP to ensure flow remain choked across bang-bang
Assumed thermal dwell from COPV loading diminished over time – COPV starts at 70F
Gating vent config was lox boiloff + emergency depress, so switch to methane didn’t change gating vent config

## Slide 12: System Design
Constrained by space, driven by top-level vehicle sizing
Consolidated into three manifolds:
  Vent manifold (one per tank due to LOx feedline positioning)
  Press/fill manifold milled from a single block of Al6061
Vent manifold distinct from press manifold
Worked around accessibility and tool constraints
Removed instrumentation I originally thought we needed

## Slide 13
Four main interfaces:
  Helium Fill
  COPV
  Ox Press
  Fuel Press
Everything had to fit within 6.625” diameter (less cover panels)
Had to use min-length tubes to fit size requirements
Dozens of iterations – produced four versions
Bang-Bang Manifold

## Slide 14: Manufacturing
Driving factor: cost
Didn’t have access to cheap additive manufacturing, so everything had to be manufacturable on a 5-axis CNC
Manifolds milled from Al6061 (for cost + machinability)
Had a single ~5” bore that required a specialized bit

## Slide 15: Bang-Bang Test Campaign
Goals:
  Validate solenoids (flow rate, cycle time, thermal capability)
  Stand up GSE sled (boost pump activation + general activation), labview and Avi for the first time
  Write procedures that would be adapted into full vehicle ops
  Gain experience with cryo ops and get everyone excited about “hardware mode”
2x Short-duration, low-pressure GN2 test
2x Full-duration, 6ksi GN2 test
Notes: Built a test tank out of sch40 steel pipe + endcaps (MEOP 318psi, orifice: 0.138”)

## Slide 16: Integrated Vehicle Ops
Performed as a Test Operator
Tests completed:
  2x Cold flows
  2x hotfires (hotfire 2 aborted after losing runline PTs due to uncontrolled flame)
First full vehicle tests with actual procedures
What to do when something goes wrong
Triple the timeline and accept some leaks
Clear comms and overcommunication saves time and commodities
Notes: Ox press valve saw degraded performance (maybe ice?) on second hotfire (full duration). Seemed to fail shut and developed longer cycle times than expected.

## Slide 17: Review
I was the RE for CMS’s Upper Plumbing and took the system through design, manufacturing, integration, test, and to full vehicle hotfires
I led testing ops, wrote procedures, and led data reviews for our first pressurized tests
I led (most) manufacturing and integration for the Upper Plumbing system

## Slide 18
Thank You!

## Slide 19: Backup Slides

## Slide 20: Burst disk FOD impact

## Slide 21: Venturi Mass Flow Equation: Sizing Sim
Venturi mass flow:

## Slide 22: Passive Relief
One ullage burst disk per tank set to burst at proof pressure - 30psi (549 psi)
  30psi to account for burst pressure uncertainty
  Size for flow rate equal to full open bang-bang valves x 1.5
Relief valve on LOx and LNG tank set to 386 psi
  Size for flow rate equal to one full open solenoid

## Slide 23: Burst Disk Sizing
Parameter | COPV | Tank
Helium Pressure | 4950 psi | 326 psi
Helium Temp | 70 F | -235 F ()
Parameter | Value
Min Cv | .12
Max SCFM = 473 SCFM

## Slide 24: BCLS